| Capacity | 1KVA |
| --- | --- |
| Input | Voltage | Single phase 100-120V or 200-240Vac |
|  | Frequency | 50Hz or 60Hz +/- 5% |
| Output | Voltage (adjustable) | Single phase 110V+20% or 220Vac +/- 20% |
|  | Frequency | 50Hz or 60Hz, 400Hz (option) +/- 0.5% |
|  | Voltage Regulation | +/- 1% |
|  | Transient Response | +/- 3% (100% load variation) |
|  | Waveform | Sinewave, THD < 3% at 0-100% linear load |
|  | Overload Capacity | 105% load 60 seconds, >150% auto transfer to bypass |
| Efficiency | AC to AC | >85% |
| Protection | Short Circuit | Current Limited and cut-off and fuse and breaker |
|  | EMI/EMC | EN50091-2, CE Approved |
| Audible Alarm | Mains Failure | Sounding every four seconds after mains fail, 90 seconds mute |
|  | Optional Battery Low | Sounding once every second as optional battery low level approaches |
|  | Overload & UPS Fault | Continuously |
| Indicator | LCD | I/P&O/P voltage, I/P&O/P frequency, |
|  | LED | 50Hz, 60Hz, Overload, Fault |
| Interface | Contact Closure | Support MEGATEC RUPS UPS monitoring software |
|  | RS-232 | Support MEGATEC RUPSII / UPSilon 2000 monitoring software |
| Environment | Operation Temperature | 0-40 degree C; 32-104 degree F |
|  | Relative Humidity | 20-90% non-condensing |
|  | Audible Noise | Less than 45dB(at 1 meter) |
| Physical | Net Weight (KGS/LBs) | 20kgs w/o battery |
|  | Dimension (WxHxD)mm | 180 x 308 x 381 |
| * Specifications are subjected to change without prior notice. |