| Capacity | 3.75KVA |
| --- | --- |
| Input | Voltage | single phase 220Vac -20% +35% |
|  | Frequency | 50Hz or 60Hz +/- 5% |
| Output | Voltage | single phase 220Vac +/- 5% (adjustable) |
|  | Frequency | 50Hz or 60Hz, 400 Hz (option) +/- 0.5% |
|  | Voltage Regulation | +/- 1% |
|  | Frequency Stability | +/- 0.5% (Free Running) |
|  | Transient Response | +/- 3% (100% load variation) |
|  | Waveform | Sinewave THD < 3% at 0-100% linear load |
|  | Overload Capacity | 120% load 30 seconds, >150% constant power. |
|  | Power factor | 0.7-1, lag |
|  | Crest ratio | 3 : 1 |
| Efficiency | AC to AC | >85% |
| Protection | Overload | 150% 30sec. |
|  | Short Circuit | Current Limited and cut-off and fuse and breaker |
|  | EMI/EMC | EN50091-2, CE Approved |
| Audible Alarm | Mains Failure | Sounding every four seconds after mains fail, 90 seconds mute |
|  | Overload | Continuously |
| Indicator | LCD | I/P&O/P voltage, I/P&O/P frequency, Loading %, History record |
|  | LED | Utility LED (green), Inverter LED (green), Fault LED (red), Overload (yellow) |
| Interface | Contact Closure | Support MEGATEC RUPS UPS monitoring software |
|  | RS-232 | Support MEGATEC RUPSII / UPSilon 2000 monitoring software |
| Environment | Operation Temperature | 0-40 degree C; 32-104 degree F |
|  | Relative Humidity | 20-90% non-condensing |
|  | Audible Noise | Less than 45dB(at 1 meter) |
| Physical | Net Weight (KGS/LBs) | 60kgs w/o battery |
|  | Dimension (WxHxD)mm | 230 x 685 x 578 |
| * Specifications are subjected to change without prior notice. |