| PHASE | 3-Phase Input / 3-Phase Output |
| --- | --- |
| KVA | 240 | 320 |
| Picture (click the picture to see big picture) |  |
| INPUT (RECTIFIER) Input Voltage | 208V /220V / 380V / 400V /415V /440V /460V /480V / 600V |
| Input Range | + / - 20% ( > +/- 20% is available upon request) |
| Input Frequency | 50 / 60 Hz + / - 5Hz |
| Power Walk In | 0% - 100% : 20 sec |
| Efficiency | > 98% |
| Voltage Regulation | + / - 1% |
| INVERTER |  |
| Output Voltage | 208V /220V / 380V / 400V /415V /440V /460V , + / - 1 % |
| Wave Form | Sine Wave |
| Output Power Factor | 0.8 |
| Output Frequency (Free Running) | 50 / 60 / 400Hz + / - 0.1 Hz |
| Phase Shift Under 100% Unbalance Load | < 0.5° |
| THD (Linear Load) | < 2 % |
| Overload | <110% | Continuous |
|  | 110 C 125% | 15 minutes |
|  | 125 C 150% | 10 minutes |
|  | > 150% | 1 minute |
| Efficiency (100% Load) | 95% | 95% |
| OVERALL CHARACTERISTICS |  |
| Overall Efficiency | 93% | 93% |
| Maximum Heat Dissipation (Kw) | 13 | 17.4 |
| Height x Width x Depth (mm) | 1600 x 2200 x 800 |
| Weight (Kg, without battery) | 1950 | 2450 |
| Audible Noise | < 67 dBA (At 1 M) |
| Temperature | 0 – 40℃ ( 32 – 104℉ ) |
| Humidity | 0% - 90% (Non-Condensing) |
| Altitude | <1500 M Above Sea Level |
| EN50091-1,-2 | YES |
| Short Circuit Pretection | YES |
| Lightning / EMC Filter | MOV / Input&Output (FCC CLASS A) |
| Galvanic Isolation | Input&Output true Galvanic isolation |
| LED,LCD,Buzzer | YES |
| Remote Control / Communication Interface | Monitoring 1~99 UPS simultaneously / Dry contact, RS232, RS485 |
| . Different specifications required are available. . All specifications mentioned above are subject to change without prior notice. |