| Model |  | AHS-503 | AHS-603 | AHS-803 | AHS-114 |
| --- | --- | --- | --- | --- | --- |
| Capacity | VA / Watt | 5KVA/4000W | 6KVA/6000W | 8KVA/8000W | 11KVA/11kW |
| Input | Nominal Voltage | 110/115/120Vac or 220/230/240Vac | 220/230/240Vac |
|  | Voltage Range | Acceptable Voltage Range | 60~135Vac or 120~270Vac | 120~270Vac |
|  |  | Frequency | 45Hz ~ 70Hz Auto-sensing |
|  |  | Low Voltage Transfer | 60Vac+/-2% ; 120Vac+/-2% | 120Vac+/-2% |
|  |  | Low Voltage Return | 65Vac+/-2% ; 130Vac+/-2% | 130Vac+/-2% |
|  |  | High Voltage Transfer | 135Vac+/-2% ; 270Vac+/-2% | 270Vac+/-2% |
|  |  | High Voltage Return | 130Vac+/-2% ; 260Vac+/-2% | 260Vac+/-2% |
| Output | Voltage |  | 110/115/120Vac or 220/230/240Vac re-settable via LCD panel |
|  | Voltage Regulation(Bat. Mode) | <3% RMS for entire battery voltage range |
|  | Frequency Regulation | Line Mode | Synchronized to AC Main |
|  |  | Battery Mode | 50Hz or 60Hz ±0.1Hz |
|  | Power Factor | 0.8 | 1.0 |
|  | Wave Form | Pure Sine wave |
|  | Effeciency | >80% |
|  | Overload Protection | Line Mode | >110%,then Buzzer Alarm and Amber LED Blink Continuously. |
|  |  | Battery Mode | 110%~150% for 30 sec; >150% for 200ms, then UPS Shuts Down |
|  | Short Circuit Protection | Line Mode | Circuit Breaker |
|  |  | Battery Mode | Electronic Circuit |
| DC Start | Cold Start | Yes |
| Transfer Time | Typical | < 8 ms. |
| Battery | Battery Voltage | 24Vdc | 48Vdc |
|  | Backup Time | Base on the batteries connected |
|  | Recharging Current | >60A |
| Control Panel | LCD Display | UPS status, I/P&O/P Voltage Frequency, Load Level, Battery Voltage & Level, Temperature, Model |
|  | LED Display | Normal (Green), Warning (Amber), Fault (Red) |
| Audible Alarm | Battery Mode | Beeping every 4 seconds |
|  | Low Battery | Beeping every second |
|  | UPS Fault | Beeping Continuously |
|  | Overload | Beeping twice per second |
| Parameter Re-settable | Voltage,Frequency,5 steps Charge current |
| Environment | Operation Temperature | 0-40 degree C; 32-104 degree F |
|  | Relative Humidity | 0-95% non-condensing |
|  | Audible Noise | Less than 55dBA (at 1M) |
| Physical | Wall Mounted Type(W*H*D)mm | 415*600*260 | 415*600*260 | 415*600*260 | 580*520*790 |
|  | Wall Mounted Type Net Weight (Kgs) | 49.2 | 51.4 | 53.6 | 94.8 |
| Safety Conformance | Safety Standard |  | EN62040-1-1 |
|  | EMC | EN62040-2 |
|  | Marks | CE |

Mark: Specifications are subjected to change without prior notice ( 090728).