| PHASE | 3-Phase Input / 1-Phase Output |
| --- | --- |
| KVA | 20 | 30 | 40 | 50 |
| DC INPUT |  |
| Input Voltage | 110V, 220V, 396V |
| INVERTER |  |
| Output Voltage | 220 / 230 / 240 V, 1Φ2ωor3ω |
| Wave Form | Sine Wave |
| Output Power Factor | 0.8 |
| Frequency Lock Range | 50 / 60 Hz + / - 3Hz |
| Output Frequency (Free Running) | 50 / 60 Hz + / - 0.1 Hz |
| Phase Shift Under 100% Unbalance Load | < 0.5° |
| THD (Linear Load) | < 2 % |
| Overload | <110% | Continuous |
|  | 110 – 125% | 15 minutes |
|  | 125 – 150% | 10 minutes |
|  | > 150% | 1 minute |
| Efficiency (100% Load) | 93% | 93% | 93.5% | 93.5% |
| STATIC SWITCH |  |
| Voltage Range | 173-277 VAC (L-N) |
| Mains ←→ Inverter | 0 ms |
| OVERALL CHARACTERISTICS |  |
| Overall Efficiency | 91% | 91% | 91.5% | 92% |
| Audible Noise | < 65 dBA (At 1 M) |
| Temperature | 0 – 40℃ ( 32 – 104℉ ) |
| Humidity | 0% - 90% (Non–Condensing) |
| Altitude | <1500 M Above Sea Level |
| EN50091-1,-2 | YES |
| Short Circuit Pretection | YES |
| Lightning / EMC Filter | MOV / Input&Output (FCC CLASS A) |
| Galvanic Isolation | Input&Output true Galvanic isolation |
| LED,LCD,Buzzer | YES |
| Remote Control / Communication Interface | Monitoring 1~99 UPS simultaneously / Dry contact, RS232, RS485 |
| . Different specifications required are available. . All specifications mentioned above are subject to change without prior notice. |