| PHASE | 3-Phase Input / 3-Phase Output |
| --- | --- |
| KVA | 80 | 100 | 120 | 160 |
| DC INPUT |  |
| Input Voltage | 110V, 220V, 396V |
| INVERTER |  |
| Output Voltage | 220V / 380V / 460V, 208VY / 380VY / 400VY / 415VY, + / - 1 % |
| Wave Form | Sine Wave |
| Output Power Factor | 0.8 |
| Frequency Lock Range | 50 / 60 Hz + / - 3Hz |
| Output Frequency (Free Running) | 50 / 60 Hz + / - 0.1 Hz |
| Phase Shift Under 100% Unbalance Load | < 0.5 |
| THD (Linear Load) | < 2 % |
| Overload | <110% | Continuous |
|  | 110 C 125% | 15 minutes |
|  | 125 C 150% | 10 minutes |
|  | > 150% | 1 minute |
| Efficiency (100% Load) | 94.5% | 94.5% | 95% | 95% |
| STATIC SWITCH |  |
| Voltage Range | 173-277 VAC (L-N) |
| Mains Inverter | 0 ms |
| OVERALL CHARACTERISTICS |  |
| Overall Efficiency | 92.5% | 92.5% | 93% | 93% |
| Audible Noise | < 67 dBA (At 1 M) |
| Temperature | 0 C 40 ( 32 C 104H ) |
| Humidity | 0% - 90% (Non-Condensing) |
| Altitude | <1500 M Above Sea Level |
| EN50091-1,-2 | YES |
| Short Circuit Pretection | YES |
| Lightning / EMC Filter | MOV / Input&Output (FCC CLASS A) |
| Galvanic Isolation | Input&Output true Galvanic isolation |
| LED,LCD,Buzzer | YES |
| Remote Control / Communication Interface | Monitoring 1~99 UPS simultaneously / Dry contact, RS232, RS485 |
| . Different specifications required are available. . All specifications mentioned above are subject to change without prior notice. |