| Model (LCD Series) | AHA-603H | AHA-104H | AHA-3104H | AHA-3154H | AHA-3204H |
| --- | --- | --- | --- | --- | --- |
| Input | Capacity | 6KVA/4200W | 10KVA/7000W | 15kVA/10500W | 20kVA/14000W |
|  | Phase | Single Phase | 3 Phase |
|  | Nominal Voltage | 1P2W 220Vac | 3P4W 380Vac |
|  | Voltage Range | 176-276Vac ±3Vac | 304-478 VAC |
|  | Frequency | 50Hz / 60Hz ±4Hz |
|  | Power Factor | ≧0.98 | ≧0.95 |
| Output | Voltage | 220VAC ± 1% (230V or 240V re-settable via LCD panel) |
|  | Frequency | Synchronized ( Line mode); 50Hz or 60Hz +/-0.5% (Battery mode) |
|  | Wave-form | True Sine wave |
|  | Distortion | Tower | ≦4% (linear load) ≦7% non-linear load) |
|  |  | Rack | 4% (linear load) , ≦7% non-linear load) | N/A |
|  | Overload Capacity | 108%~130%: 10mins , UPS go Bypass . > 130% : 1 sec , UPS go Bypass ; 1 min, UPS shutdown. |
|  | Crest Ratio | 3: 1 |
| Battery | DC Voltage | 240V |
|  | Capacity | 12V/ 7Ah X 20pcs | 12V/ 9Ah X 20pcs | Depend on the capacity of external batteries |
|  | Back-up Time | ＞8 min. | ＞5 min. | Depend on the capacity of external batteries |
| Charger | Built-In /Option | 2Amp/4.2Amp (2 steps) | 2Amp/4.2Amp (2 steps) |
|  | Recharging Time | 7 hrs to 90% | 8 hrs to 90% | Depend on the capacity of external batteries |
| Bypass | Automatic | Overload or UPS fault |
|  | By setting | NA |
|  | Transfer Time | 0 ms (AC to DC & inverter to bypass) |
| Indicator | LCD (Series) | UPS status, I/P&O/P Voltage & Frequency ,Load %, Battery Voltage, Battery Capacity % ,Temperature, Model Spec., Event Log. LED: Normal (Green), Warning (Yellow), Fault (Red) |
|  | LED (Series) | Normal (Green), Bypass(Yellow), Battery Low (Yellow), Inverter (Green), Load% (5 LEDs), Battery % (5 LEDs), Fault(Red) |
| Outlet | Tower | Terminal Blocks |
|  | Rack | Terminal Blocks |
| Audible Alarm | Battery Mode | Beeping every 4 seconds (re-settable) |
|  | Battery Low | Beeping every seconds |
|  | Overload | Beeping twice per second |
|  | Fault | Beeping Continuously |
| Interface | RS-232 Interface | UPSilon2000 monitoring software for Windows all, Unix systems and Novell. |
|  | Multi-Interface Slot | SNMP card, AS 400, Dry Contact, USB Selectable |
| Network | Surge Protection | N/A |
| Parallel | Available (Option) |
| Environment | Temperature | 0~40℃; 32~104℉ |
|  | Humidity | 0-95% non-condensing |
|  | Acoustic Noise | ＜55 dBA (at 1 M) | ＜60 dBA (at 1 M) |
| Physical | Weight (w/o Battery | 35 kgs | 38kgs | 38.5kgs | 55kgs | 55kgs |
|  | Weight (w/ Battery) | 90 kgs | 93kgs | --- | --- | --- |
|  | Dimension W*H*D | Tower | 260 x 717 x 570mm |
|  |  | Rack | 482.6 x 176 (4U) x 600mm (Rack) | NA |
|  | Color | White or Black |

- Tower Series: AHA-H, Rack Series: AHA-HR

- Rack Battery Bank (2U) is available for 8pcs (1 set) 12V/7Ah and 9pcs (3 sets) 12V/7Ah batteries.

- Specifications are subject to change without notice.